Title
Update on the Software Correlator
Nico Kruithof, Huseyin Özdemir, Yurii Pydoprihora,
Ruud Oerlemans, Mark Kettenis, JIVE

---
Starting Point
Starting Point
C++ implementation of the correlator used for the Huygens
FX correlator.
Monolithic.
Single-subband, USB only.
Single-threaded, largey unoptimized.
Driven by home-grown control file.
No integrated delay model.
No fringes on standard EVN data.
Input data needs conversion.
Raw output data.

---
Design Decisions
Design Decisions
Parallelisation in both subbands and time.
All baselines for a single subband processed on a single cluser node.
Further course grained parallelisation (in time only) to distribute over multiple clusters.
Input node (one per station)
Correlator node (as many as feasable)
Output node
Manager node

---
Design Decisions (2)
Design Decisions
Telescopes
Grid
Input nodes
Time and channel slicing
Correlator nodes
Sorting and merging
Output node

---
Current State
Current State
VEX-driven, with small JSON-based control file specifying correlation parameters.
Modular.
Parallelized using MPI.
Scales from SMP machines to largish clusters.
Integrated delay model based on CALC 10.
All subbands processed, both LSB and USB, cross-correlations.
Still mostly unoptimized: 2.5 min to process 1s of a typical EVN NME on a quadcore SMP machine.
Takes Mark4 (Mark5A) input data.
Output data format that includes (some) metadata.

---
Validation (1)
Validation
Phase Closure

---
Validation (2)
Validation
Noise Analysis

---
Validation (3)
Validation
Comparison with the Hardware Correlator

---
Optimization
Optimization
Use single-precision where possible (all double precision now)
Input data conversion using lookup tables.
Use Intel/AMD vector libraries.
Fringe rotation before fractional bit shift.
Fringe rotation after correlation.

---
FTP Fringe Test
Success Story: FTP Fringe Tests
Cluster running NICT correlator broke down in May
SFXC was used for May/Jun and Oct/Nov FTP Fringe Tests

---
Post Processing
Post Processing
JIVE uses j2ms2 to convert hardware correlator output into MeasurementSet.
J2ms2 has been adapted to accapt old SFXC output format.
Currently being adapted to accept new SFXC output format.
Translation into FITS through standard pipeline.

---
The Bigger Picture
The Bigger Picture
How to get things on the Grid?
Workflow Manager (PSNC)
VLBI Grid broker (PSNC)
Web Services
  - Vex2ccf: Creates control file template from VEX
  - Data providers: Provides chunks of data and transfers them to GridFTP servers.

---
The Picture
The Picture

---
Future Directions
Future Directions
Make things faster
Real-Time eVLBI
Accept Mark5B Input Data
SCARIe: Running SFXC on DAS-3 & Startplane