JUC Design Review
The Delay Model
or
The fun you can have
without floating point arithmetic

---
Introduction
- Uniboard has only integer arithmetic
  - Counts as fixed-point if you squint
- Control system supplies delay & phase info
  - Quadratic poly coeffs for each integration
  - Evaluated on UniBoard
- Need to be careful about dynamic range
- Accuracy limited by phase-rotator module

---
Pipeline (off-board)
- Experiment database
- CALC (“industry standard”)
  - Delays at 1s intervals
- Calculate phase delays
- Polynomial fitting
- Coordinate transform (ticks)
- Shifting and discretizations
- Packetization and dispatch

---
On Uniboard
To correlator
Data
(FFT Segments)
Polyphase
Filter Bank
Fractional
Delay corrector
Phase model
Delay model
Fractional delay
Downshift
Phase
correction
Integer delay
Phase rotation
vector

---
Accuracy (Overview)
- No floating point
  - Need to choose fixed point precisions carefully
  - Need to discretize phase delays separately
- Space VLBI (RadioAstron) changes things
  - A lot (2 s delay instead of 0.02 s)
  - Really a lot (50 μs/s delay rate instead of 1.6 μs/s)

---
Accuracy (delay)
- Limited by phase rotation module (8 bits)
- Constant delay term currently 8-bits after b.p.
  - Legacy detail; not enough bits
  - Numerical expts show we need 12 bits
- Delay rate rescaled (shift left by 31 bits)
- Quadratic term not important over 1s interval

---
Recommendations
- Mostly still pending
- Delay
  - Linear polynomial over integration
  - 48-bit coefficients
  - Constant term 8-bit FP
  - Linear term 32-bit FP
- Phase
  - Quadratic polynomial over integration
  - 64-bit coefficients, 64-bit FP

---
Accuracy (phase)
- Phase delay is just delay×frequency
- Polynomials offboard where floats available
- Separate quad poynomial for each subband
- Phase calculated in units of cycles
- Integer part discarded (=mod 2π)
- 9 msb used for PolyphaseFilterBank
- Need 60-bit coefficients for 1s interval
  - (Currently have 48 bits)